## Slide 1: The “Greedy Snake” Algorithm
Nick Govier
David Newman

## Slide 2: Overview
What is “Greedy Snake”?
How does it Work?
Problems of Greedy Snake
References
Demo
Questions??

## Slide 3: What is “Greedy Snake”?
A Feature Extraction technique
Sometimes called “Active Contours”
Works like stretched Elastic Band being released

## Slide 4: “Greedy Snake” Theory (1)
Initial Points defined around Feature to be extracted
  Explicitly defined
  Approximation of an Ellipse
Pre-defined number of Points generated

## Slide 5: “Greedy Snake” Theory (2)
Points are moved through an Iterative Process
“Energy Function” for each point in the Local Neighbourhood is calculated
Move to point with lowest Energy Function
Repeat for every point
Iterate until Termination Condition met
  Defined number of iterations
  Stability of the position of the points

## Slide 6: Energy Function
Three Components
  Continuity
  Curvature
  Image (Gradient)
Each Weighted by Specified Parameter
Total Energy = α · Continuity + β · Curvature + γ · Image

## Slide 7: Continuity
Abs(avg_dist_btw_nodes – dist(V(i),V(i-1))
Value = Smaller Distance between Points
The higher α, the more important the distance between points is minimized
Neighbouring Points
Current Point
Possible New Points

## Slide 8: Curvature
Norm(V(i-1) -2·V(i) + V(i+1))2
Normalised by greatest value in neighbourhood
The higher β, the more important that angles are maximized
Neighbouring Points
Current Point
Possible New Points

## Slide 9: Image (Gradient)
- Img_grad (V(i))
High Image Gradient = Low Energy value
The higher γ, the more important image edges are
Assume Gradient Measured on 3x3 Template
Low Image Gradient
High Image Gradient

## Slide 10: Drawing Corners
For each Snake Point take Curvature Value
IF Greater than other points
  AND specified Angular Threshold
  AND Image Gradient high enough
THEN set β for that Snake point to 0, allowing a Corner

## Slide 11: Varying α, β and γ
Choose different values dependent on Feature to extract
Set α high if there is a deceptive Image Gradient
Set β high if smooth edged Feature, low if sharp edges
Set γ high if contrast between Background and Feature is low

## Slide 12: “Greedy Snake” Problems
Very sensitive to Noise
  Both Gaussian and Salt & Pepper
Before defining initial points
  Firstly Gaussian Blur image
  Then apply a Median Filter

## Slide 13: References
[1]:http://www.markschulze.net/snakes/ - Snake Applet & Explanation of Algorithm
[2]:http://torina.fe.uni-lj.si/~tomo/ac/Snakes.html - Another Snake Applet
[3]:http://web.mit.edu/stanrost/www/cs585p3/p3.html – Explanation + Matlab Implementation
[4]:http://homepages.inf.ed.ac.uk/cgi/rbf/CVONLINE/entries.pl?TAG709 – Repository of Greedy Snake Links

## Slide 14: Demo
www.ecs.soton.ac.uk/~drn101/Snakes.html

## Slide 15: Questions ??